## Slide 1: PID
Ara Kourchians

## Slide 2
Physical
World
Desired
World
Control

## Slide 3: Open Loop
Physical
World
Desired
World
Control
Notes: Simple autonomous mode that follows a script
Sprinkler system on a timer
Motor + battery
You “trust” that it works and assume ideal conditions

## Slide 4: Closed Loop
Physical
World
Desired
World
Control
Sensing
Notes: Air Conditioners
Airplanes auto-pilot
Drones

## Slide 5: ??? Loop
Notes: - Based on the previous definition, is this a closed or open loop system?

## Slide 6: Closed Loop
Sensing
X

## Slide 7: Closed Loop
Sensing
Control
X
Notes: - Explain how the students observe where the robot is and come up with a control command to give the robot, but this has a problem….

## Slide 8: Closed Loop
Sensing
Control
X
Notes: This requires training, learning, ‘piloting’
Robot might not drive perfectly straight
Might slip, or be going uphill and will require the driver to manually add more power
So far, the driver has had to learn each robot.. and every robot is different

## Slide 9: Some terminology
Error
Target
State
Motor
Encoder
Notes: The story is different for autonomous mode

## Slide 10: Autonomous Mode
Error
Target
State
X
Notes: The story is different for autonomous mode

## Slide 11: Autonomous Mode
Error
Target
State
X
autonomous.c

## Slide 12: Autonomous Mode
autonomous.c
void go()
{
..
robot.drive(X);
..
}
X
0
Notes: How do you actually write this in terms of motors and sensors?

## Slide 13: Autonomous Mode
Error
autonomous.c
void go()
{
..
robot.motors(100);
wait(1_SEC);
robot.motors(0); ..
}
X+Error
X
0

## Slide 14: Autonomous Mode
Error
autonomous.c
void go()
{
..
robot.motors(100);
while(encoder < 1000)
{
encoder = robot.read();
}
robot.motors(0);
..
}
X+Error
X
0
Notes: You’re going to overshoot when you get to your goal (100% to 0%)

## Slide 15: PID Control
Error
0

## Slide 16: PID Control
Proportional
Present
P*Error
Integral
Past
I*Sum_of_Errors
Derivative
Future
D*(Error- Last_Error)
5
2
1
5
2
1
+
+
Notes: PID controllers run in a loop, it’s iterative
Weights of each term depend on the system!
The P, I, and D terms are summed and used as the controller output

## Slide 17: Position Control Using PID

## Slide 18: PID Block Diagram
P
Motor
Σ
I
D
+
+
+
-
+
Target
State
Error
Output

## Slide 19: PID Block Diagram
P
Motor
Σ
I
D
+
+
+
-
+
Target
State
Error
Output
Encoder

## Slide 20: Proportional Control

## Slide 21: Proportional Control
Error
0
Motor = P * Error

## Slide 22: Proportional Control
Error
0
Motor = P * Error
100 = 2 * 50

## Slide 23: Proportional Control
Error
0
Motor = P * Error
20 = 2 * 10

## Slide 24: Proportional Control
Error
0
Motor = P * Error
1 = 2 * 1
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 25: Proportional Control

## Slide 26: Integral Control

## Slide 27: Integral Control
Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 28: Integral Control
Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 29: Integral Control
Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 30: Integral Control
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 31: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 32: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 33: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 34: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-75 = -35 + -40
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-38 = 0.5 * -75
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 35: Integral Control

## Slide 36: Derivative Control

## Slide 37: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
= 0.5 * (50 – 0)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 38: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
25 = 0.5 * (50 – 0)
-5 = 0.5 * (40 – 50)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 39: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
25 = 0.5 * (50 – 0)
-5 = 0.5 * (40 – 50)
-2.5 = 0.5 * (35 – 40)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 40: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
25 = 0.5 * (50 – 0)
-5 = 0.5 * (40 – 50)
-2.5 = 0.5 * (35 – 40)
0 = 0.5 * (35 – 35)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 41: Derivative Control

## Slide 42: PID Plot Terminology

## Slide 43: PID Plot Terminology
Rise Time
Settling Time
Overshoot
Steady-State Error

## Slide 44: P = 50

## Slide 45: P = 100

## Slide 46: P = 300

## Slide 47: I = 10

## Slide 48: I = 50

## Slide 49: I = 80

## Slide 50: D = 10

## Slide 51: D = 100

## Slide 52: PID Tuning Methods

## Slide 53: PID Plot Terminology
Rise Time
Settling Time
Overshoot
Steady-State Error

## Slide 54: PID Tuning Methods
Parameter Increase | Rise Time | Overshoot | Settling Time | Steady-State Error
Kp |  |  | Small Change | 
Ki |  |  |  | 
Kd | Small Change |  |  | Small Change

## Slide 55: P = 30, I = 0, D = 0

## Slide 56: P = 30, I = 15, D = 0

## Slide 57: P = 30, I = 30, D = 0

## Slide 58: P = 30, I = 60, D = 0

## Slide 59: P = 30, I = 80, D = 0

## Slide 60: P = 30, I = 70, D = 0

## Slide 61: P = 30, I = 70, D = 10

## Slide 62: P = 30, I = 70, D = 1

## Slide 63: DEMO!

## Slide 64: Hardware