## Slide 1: PID Sensing and Control Systems
Ara Kourchians

## Slide 2
Physical
World
Desired
World
Control

## Slide 3: Open Loop
Physical
World
Desired
World
Control
Notes: Simple autonomous mode that follows a script
Sprinkler system on a timer
Motor + battery
You “trust” that it works and assume ideal conditions

## Slide 4: Closed Loop
Physical
World
Desired
World
Control
Sensing
Notes: Air Conditioners
Airplanes auto-pilot
Drones

## Slide 5: ??? Loop
Notes: - Based on the previous definition, is this a closed or open loop system?

## Slide 6: Closed Loop
Sensing
X

## Slide 7: Closed Loop
Sensing
Control
X
Notes: - Explain how the students observe where the robot is and come up with a control command to give the robot, but this has a problem….

## Slide 8: Closed Loop
Sensing
Control
X
Notes: This requires training, learning, ‘piloting’
Robot might not drive perfectly straight
Might slip, or be going uphill and will require the driver to manually add more power
So far, the driver has had to learn each robot.. and every robot is different

## Slide 9: Some terminology
Error
Target
State
Motor
Encoder
Notes: The story is different for autonomous mode

## Slide 10: Autonomous Mode
Error
Target
State
X
Notes: The story is different for autonomous mode

## Slide 11: Autonomous Mode
Error
Target
State
X
autonomous.c

## Slide 12: Autonomous Mode
autonomous.c
void go()
{
..
robot.drive(X);
..
}
X
0
Notes: How do you actually write this in terms of motors and sensors?

## Slide 13: Autonomous Mode
Error
autonomous.c
void go()
{
..
robot.motors(100);
wait(1_SEC);
robot.motors(0); ..
}
X+Error
X
0

## Slide 14: Autonomous Mode
Error
autonomous.c
void go()
{
..
robot.motors(100);
while(encoder < 1000)
{
encoder = robot.read();
}
robot.motors(0);
..
}
X+Error
X
0
Notes: You’re going to overshoot when you get to your goal (100% to 0%)

## Slide 15: PID Control
Error
0

## Slide 16: PID Control
Proportional
Present
P*Error
Integral
Past
I*Sum_of_Errors
Derivative
Future
D*(Error- Last_Error)
5
2
1
5
2
1
+
+
Notes: PID controllers run in a loop, it’s iterative
Weights of each term depend on the system!
The P, I, and D terms are summed and used as the controller output

## Slide 17: PID in the real world

## Slide 18: Next Time…
Hardware:
October 1st
Math and Code:
October 8th

## Slide 19: Next Time…

## Slide 20: PID
Ara Kourchians

## Slide 21
Physical
World
Desired
World
Control

## Slide 22: Open Loop
Physical
World
Desired
World
Control
Notes: Simple autonomous mode that follows a script
Sprinkler system on a timer
Motor + battery
You “trust” that it works and assume ideal conditions

## Slide 23: Closed Loop
Physical
World
Desired
World
Control
Sensing
Notes: Air Conditioners
Airplanes auto-pilot
Drones

## Slide 24: ??? Loop
Notes: - Based on the previous definition, is this a closed or open loop system?

## Slide 25: Closed Loop
Sensing
X

## Slide 26: Closed Loop
Sensing
Control
X
Notes: - Explain how the students observe where the robot is and come up with a control command to give the robot, but this has a problem….

## Slide 27: Closed Loop
Sensing
Control
X
Notes: This requires training, learning, ‘piloting’
Robot might not drive perfectly straight
Might slip, or be going uphill and will require the driver to manually add more power
So far, the driver has had to learn each robot.. and every robot is different

## Slide 28: Some terminology
Error
Target
State
Motor
Encoder
Notes: The story is different for autonomous mode

## Slide 29: Autonomous Mode
Error
Target
State
X
Notes: The story is different for autonomous mode

## Slide 30: Autonomous Mode
Error
Target
State
X
autonomous.c

## Slide 31: Autonomous Mode
autonomous.c
void go()
{
..
robot.drive(X);
..
}
X
0
Notes: How do you actually write this in terms of motors and sensors?

## Slide 32: Autonomous Mode
Error
autonomous.c
void go()
{
..
robot.motors(100);
wait(1_SEC);
robot.motors(0); ..
}
X+Error
X
0

## Slide 33: Autonomous Mode
Error
autonomous.c
void go()
{
..
robot.motors(100);
while(encoder < 1000)
{
encoder = robot.read();
}
robot.motors(0);
..
}
X+Error
X
0
Notes: You’re going to overshoot when you get to your goal (100% to 0%)

## Slide 34: PID Control
Error
0

## Slide 35: PID Control
Proportional
Present
P*Error
Integral
Past
I*Sum_of_Errors
Derivative
Future
D*(Error- Last_Error)
5
2
1
5
2
1
+
+
Notes: PID controllers run in a loop, it’s iterative
Weights of each term depend on the system!
The P, I, and D terms are summed and used as the controller output

## Slide 36: Position Control Using PID

## Slide 37: Proportional Control

## Slide 38: Proportional Control
Error
0
Motor = P * Error

## Slide 39: Proportional Control
Error
0
Motor = P * Error
100 = 2 * 50

## Slide 40: Proportional Control
Error
0
Motor = P * Error
20 = 2 * 10

## Slide 41: Proportional Control
Error
0
Motor = P * Error
1 = 2 * 1
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 42: Proportional Control

## Slide 43: Integral Control

## Slide 44: Integral Control
Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 45: Integral Control
Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 46: Integral Control
Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 47: Integral Control
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 48: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 49: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 50: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-85 = -35 + -50
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-43 = 0.5 * -85
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 51: Integral Control
-Error
0
Error_Sum = Error_Sum + Error
50 = 0 + 50
95 = 50 + 45
115 = 95 + 20
115 = 115 + 0
75 = 115 + -40
25 = 75 + -50
-35 = 25 + -60
-75 = -35 + -40
Motor = I * Error_Sum
25 = 0.5 * 50
48 = 0.5 * 95
56 = 0.5 * 115
56 = 0.5 * 115
38 = 0.5 * 75
13 = 0.5 * 25
-17 = 0.5 * -35
-38 = 0.5 * -75
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 52: Integral Control

## Slide 53: Derivative Control

## Slide 54: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
= 0.5 * (50 – 0)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 55: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
25 = 0.5 * (50 – 0)
-5 = 0.5 * (40 – 50)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 56: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
25 = 0.5 * (50 – 0)
-5 = 0.5 * (40 – 50)
-2.5 = 0.5 * (35 – 40)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 57: Derivative Control
Error
0
Motor = D* (Error – Last_Error)
25 = 0.5 * (50 – 0)
-5 = 0.5 * (40 – 50)
-2.5 = 0.5 * (35 – 40)
0 = 0.5 * (35 – 35)
Notes: You may never reach it, or overshoot it
VERY system dependent ^
P term would be target distance dependent

## Slide 58: Derivative Control

## Slide 59: PID Plot Terminology

## Slide 60: PID Plot Terminology
http://www.ni.com/cms/images/devzone/tut/a/12fbdcae1636.gif

## Slide 61: P = 50

## Slide 62: P = 100

## Slide 63: P = 300

## Slide 64: I = 10

## Slide 65: I = 50

## Slide 66: I = 80

## Slide 67: D = 10

## Slide 68: D = 100

## Slide 69: PID Tuning Methods

## Slide 70: PID Tuning Methods
http://people.ece.cornell.edu/land/courses/ece4760/FinalProjects/s2012/fas57_nyp7/Site/pidcontroller.html

## Slide 71: P = 30, I = 0, D = 0

## Slide 72: P = 30, I = 15, D = 0

## Slide 73: P = 30, I = 30, D = 0

## Slide 74: P = 30, I = 60, D = 0

## Slide 75: P = 30, I = 80, D = 0

## Slide 76: P = 30, I = 70, D = 0

## Slide 77: P = 30, I = 70, D = 10

## Slide 78: P = 30, I = 70, D = 1